## Slide 1
NETWORKING FUNDAMENTALS
Quality of Service (QoS)
Explained in Simple and Technical Terms
How networks decide what traffic gets priority — and why it matters
M.V.Preethashri
192524476

## Slide 2
INTRODUCTION
QoS is traffic management for data
Imagine an airport security line: most travelers wait in the regular queue, but urgent passengers — a diplomat, a crew member, a connecting flight about to close — get to skip ahead. QoS does the same thing for data packets crossing a network.
Without QoS, every packet is treated equally and served first-come, first-served. When the network gets busy, everything — video calls, downloads, emails — competes for the same limited space, and the things that need to arrive fast (like a voice call) can suffer just as much as the things that don't (like a background update).
Priority Lane
Voice call · Video conference
Standard Lane
Web browsing · Email
Background Lane
Backups · Software updates

## Slide 3
THE TECHNICAL DEFINITION
A formal definition
Quality of Service (QoS) is the set of technologies and mechanisms that measure and control a network's ability to give predictable performance to selected traffic — by managing bandwidth, latency, jitter, and packet loss rather than treating all traffic identically.
Classification & Marking
Identify packet type and tag it (DSCP / 802.1p) so devices downstream know its priority.
Queuing & Scheduling
Sort marked packets into queues and decide the order they leave an interface.
Shaping & Policing
Smooth or cap traffic flow to match available bandwidth and contracted rates.

## Slide 4
WHY IT MATTERS
Links have finite capacity
Every link — an office WAN connection, a home router's uplink, a data-center port — can carry only so much traffic at once. QoS decides what happens when demand exceeds that capacity.
Chart: Voice Call Jitter Under Congestion
| No QoS | With QoS
Jitter (ms) during congestion | 42 | 6
What congestion does without QoS
Voice and video calls break up, echo, or freeze
Important business traffic queues behind bulk transfers
Packet loss rises, forcing retransmissions that add more load
Users perceive the whole network as 'slow', even though total throughput may be fine

## Slide 5
KEY METRICS
What QoS actually measures
Bandwidth
How much data can flow at once
Available capacity, in bits per second, on a link or path
Latency
How long a packet takes to arrive
One-way or round-trip delay, typically in milliseconds
Jitter
How uneven the delay is
Variation in inter-packet arrival time; disrupts real-time audio/video
Packet Loss
How much data never arrives
Percentage of packets dropped, often during congestion

## Slide 6
HOW IT WORKS
From packet arrival to the wire
01
Classify
Inspect headers (port, protocol, DSCP) to identify traffic type.
02
Mark
Tag the packet (DSCP/CoS) so every hop treats it consistently.
03
Queue
Place the packet into a priority, weighted, or low-latency queue.
04
Schedule
A scheduler (e.g. WFQ, LLQ) decides transmission order per queue.
05
Shape / Police
Smooth bursts or drop/re-mark traffic exceeding contracted rates.
This pipeline runs on every QoS-aware device the packet crosses — routers, switches, and firewalls — so consistent marking end-to-end matters as much as any single step.

## Slide 7
QoS MODELS
Three approaches, three trade-offs
Best Effort
IntServ
DiffServ
How it treats traffic
All packets equal, FIFO
Reserves resources per flow
Classifies traffic into a few service classes
Scalability
Excellent — no state kept
Poor — state per flow
Good — state per class, not per flow
Guarantee level
None
Strict, end-to-end
Relative priority, not absolute
Typical use
Default Internet traffic
Small, controlled networks
Enterprise & ISP backbones

## Slide 8
TAKEAWAYS
QoS in one sentence, two ways
SIMPLE
“QoS makes sure the traffic that matters most gets through first, even when the network is busy.”
TECHNICAL
“QoS classifies, marks, queues, schedules, and shapes traffic to control bandwidth, latency, jitter, and loss for selected flows.”
Congestion is inevitable — QoS decides who waits, not whether anyone does
Marking must be consistent end-to-end, or priority is lost at the first untrusted hop
DiffServ scales; IntServ guarantees — most real networks pick DiffServ for that reason

## Slide 9
CONCLUSION
QoS turns a shared, unpredictable network
into one that behaves predictably
Bandwidth will always be finite and demand will always spike. QoS doesn't create more capacity — it makes a deliberate, policy-driven choice about who gets served first when capacity runs short, so voice, video, and business-critical traffic stay usable while everything else simply waits its turn.
Give the traffic that matters most priority when the network is busy.
Classify, mark, queue, schedule, and shape packets consistently, end-to-end.
DiffServ, for most networks — it scales without per-flow overhead.
SIMPLE IDEA
HOW
RIGHT MODEL

## Slide 10
Thank you